## Slide 1: ECE 551 Digital Design And Synthesis
Fall’17
Lecture 1
  Instructor Introduction
  Course Introduction
  Administrative Stuff
  Introduction to Verilog

## Slide 2
Instructors
Eric Hoffman
Faculty Associate
Have no PhD, Masters only
25+ years industry experience doing Integrated Circuit & System design
  10 years at Intel
  7+ years at ZMD (Mixed signal, Analog/Digital IC’s)
  8+ years as independent consultant
Instructing experience:
  ECE555, ECE552, ECE551, ECE353
Dave Schlais = TA

## Slide 3: Instructor and TA Office Hours
Eric Hoffman
  Office = EH2358, if not there then check 3654 or possibly B555
  Hours
    Mon & Weds 2:30 to 4:00 (also around other times. If door all the way open feel free)
  Email = erichoffman@wisc.edu
TA = Dave Schlais
  Office Hours = Held in B555 (basement unix lab)
    Tuesdays 1:30 – 3:00
    Available via email
  Email = schlais2@wisc.edu
Discussion Sessions hosted by Dave
  Monday (4:00 – 5:00) (TA has conflict with original time)(Room 2535)
  Tuesday 6:30 – 7:30PM, Room is 2255
  Some weeks discussion will be tutorials, in which case room is B555

## Slide 4: Course Goals
Provide knowledge and experience in:
  Digital circuit design using a HDL (Verilog & SVerilog)
  HDL simulation
  Good practices in digital design verification
    How to build self checking test benches
    How to evaluate test suite using coverage tools
  Synthesis of dataflow and behavioral designs
    Optimizing hardware designs (timing, area, power)
  Basic static timing analysis concepts
  Design tools commonly used in industry
Teach you to be able to “think hardware” first, then code it in an HDL.

## Slide 5: Course Structure (not inverted, not standard)
Some Video Lectures (with subsequent quizzes)
Some Classroom Lectures (usually one a week)
Class room exercises with: ModelSim/Quartus/Synopsys
In class exercises
  Most individual, some as team of 2, some as project team
  Verilog DUT and testbench creation & simulation
  Sometimes mapping it to Altera FPGA (DE0 Nano)
  Sometime mapping it to std cell (Synopsys)
First 2 classes will be lectures because we have to have background before exercises practical.

## Slide 6: What You Should Already Know
Principles of basic digital logic design (ECE 352)
  Number representations (unsigned, signed, Hex & Binary)
  Boolean algebra
  Gate-level design
  K-Map minimization
  Finite State Machines
  Basic datapath structures (adders, shifters, SRAM)
How to log in to CAE machines and use a Linux shell

## Slide 7: Course Website
Moodle course page: (ay17-18.moodle.wisc.edu)
What the Website will have:
  Lecture Notes (I will try to stay 1 week ahead of class)
  Lecture Videos and Quizzes
  Homework Assignments
  In Class Exercise Descriptions
  Tutorials
  Project Information
  Supplemental Information
  Midterm Solution

## Slide 8: Course Materials
Lecture Slides
No Textbook Necessary
  Can get by with the Standards & Lecture slides
Standards
  IEEE Std.1364-2001, IEEE Standard Verilog Hardware Description Language, IEEE, Inc., 2001.
  IEEE Std 1364.1-2002, IEEE Standard for Verilog Register Transfer Level Synthesis, IEEE, Inc., 2002
Synopsys on-line documentation
Other useful readings
Will have to buy a DE0 Nano FPGA board.
  Pair up with someone and buy one for group of two.
  Will sell them 3 weeks or so into the semester for $70 each.

## Slide 9: DE0-Nano (Altera FPGA Board)

## Slide 10: Evaluation and Grading
Approximately:
  12.5% Homework
  8% Quizzes on video lectures (lowest 1 score dropped)
  8% In class exercise results (lowest 2 scores dropped)
  1.5% Cummings paper quiz
  30% Project (groups of 3 or 4) (Establish team soon)
  20% Midterm
  20% Final
Homework due before of class period of due date
  15% penalty for each late period of 24 hours
  Not accepted >48 hours after deadline
  Will be done as Moodle Quizzes or dropboxes.
Graded on a curve. Class average grade will be around 3.25

## Slide 11: Class Project
Work in groups of 3 or 4 students
Design, model, simulate, synthesize, and test a complex digital system.
Several milestones
  Forming teams
  Homework problems that build toward the project
  Project status report
  Final demonstration (including mapping to your DE0 Nano)
More details coming later in the course

## Slide 12: Course Tools
Industry-standard design tools:
  Modelsim HDL Simulation Tools (Mentor)
  Design Vision Synthesis Tools (Synopsys)
  TSMC 45nm CMOS Standard Cell Technology Library
Tutorials will be available for both tools
  Modelsim tutorials next week, (only attend one of these)
    Monday 4:00 – 5:30 held in B555
    Tuesday 6:30 – 8:00 held in B555
    Wednesday 6:30 – 8:00 held in B555
  Design Vision tutorial a 6 to 7 weeks later
  Tool knowledge will be required to complete homeworks
  Dave Schlais will be a resource for help on tools

## Slide 13: ModelSim Tutorial
ModelSim is our Verilog simulator.
  Tutorial takes about 1 to 1.5 hours
  3 tutorial sessions will be held next week (only attend one)
    Monday Sept 11th 4:00 – 5:30 in B555
    Tuesday, Sept 12th 6:30 – 8:00 in B555
    Wednesday, Sept 13th 6:30 – 8:00 in B555
  You only need to attend one of these sessions!
  You can also do it on your own if you can’t make any of these sessions.

## Slide 14: What You Should Get From This Class
This class will teach you how to use Hardware Description Languages (HDLs) to design, verify, and realize digital logic
You will learn how to synthesize HDLs into hardware using the same tools used in industry
You will participate in the always enlightening process of working to design a digital system in a team environment
By the end of this course, most of you should be qualified for an entry-level job or internship at a hardware design firm ($$$)

## Slide 15
Manufacture
&
Hardware
Validation
APR, Parasitic Extraction
& Timing Checks

## Slide 16
APR, Parasitic Extraction
& Timing Checks
Manufacture
&
Hardware
Validation

## Slide 17: What is an HDL?
HDL = Hardware Description Language
  Allows for modeling & simulation (with timing) of digital designs
  Can be synthesized into hardware (netlist) by synthesis tools (Synopsys, Ambit, FPGA compilers)
  Two major standards in industry & academia
    Verilog (Flexible, loose, more common in industry)
    VHDL (Strongly typed, more common in defense and automotive)
    Having used both I prefer Verilog. This course will use Verilog
    System Verilog (Sverilog) is the next generation of verilog, and we will be learning portions of system verilog as well.

## Slide 18: What is an HDL? (continued)
module counter(clk,rst_n,cnt);
input clk,rst_n;
output [3:0] cnt;
reg [3:0] cnt;
always @(posedge clk) begin
if (!rst_n)
cnt = 4’b0000;
else
cnt = cnt+1;
end
endmodule
It looks like a programming language
It is NOT a programming language
  It is always critical to recall you are describing hardware
  This codes primary purpose is to generate hardware
  The hardware this code describes (a counter) can be simulated on a computer. In this secondary use of the language it does act more like a programming language.

## Slide 19: Simulating/Validating HDL
The sad truth…
  10% design, 90% validation
  If you do it right you will spend 9X more time testing/validating a design than designing it.
Design
Under Test
(verilog)
Stimulus
Generation
(verilog)
Output
Monitoring
Self Checking
(verilog)
file
file
Verilog test bench shell
Testbenchs are written in verilog as well.
Testbench verilog is not describing hardware and can be thought of as more of a program.

## Slide 20: What is Synthesis?
Takes a description of what a circuit DOES
Creates the hardware to DO it
module counter(clk,rst_n,cnt);
input clk,rst_n;
output [3:0] cnt;
reg [3:0] cnt;
always @(posedge clk) begin
if (~rst_n)
cnt = 4’b0000;
else
cnt = cnt+1;
end
endmodule
Synthesis Tool
(Synopsys)
Increment
Combinational
Logic
rst_n
4
4
4
clk
cnt[3:0]
Output is actually a text
netlist, not a GUI schematic
form.

## Slide 21: Synthesizing the Hardware Described
All hardware created during synthesis
  Even if a is true, still computing d&e
Learn to understand how descriptions translated to hardware
if (a) f = c & d;
else if (b) f = d;
else f = d & e;
f
a
b
c
d
e

## Slide 22: Why Use an HDL?
Enables Larger Designs
  More abstracted than schematics, allows larger designs.
    Register Transfer Level Description
    Wide datapaths (16, 32, or 64 bits wide) can be abstracted to a single vector
    Synthesis tool does the bulk of the tedious repetitive work vs schematic capture
  Work at transistor/gate level for large designs: cumbersome
Portable Design
  Behavioral or dataflow Verilog can be synthesized to a new process library with little effort (i.e. move from 0.11m to 45nm process)

## Slide 23: Why Use an HDL? (continued)
Explore larger solution space
  Synthesis options can help optimize (power, area, speed)
  Synthesis options and coding styles can help examine tradeoffs
    Speed
    Power
    area
Portable Design (continued)
  Verilog written in ASCII text. The ultimate in portability. Much more portable than the binary files of a GUI schematic capture tool.

## Slide 24: Why Use an HDL? (continued)
Better Validated Designs
  Verilog itself is used to create the testbench
    Flexible method that allows self checking tests
    Unified environment
  Synthesis tools are very good from the boolean correctness point of view
    If you have a logic error in your final design there is a 99.999% chance that error exists in your behavioral code
    Errors caused in synthesis fall in the following categories
      Timing
      Bad Library definitions
      Bad coding style…sloppyness

## Slide 25: Other Important HDL Features
Are highly portable (text)
Are self-documenting (when commented well)
Describe multiple levels of abstraction
Represent parallelism
Provides many descriptive styles
  Structural
  Register Transfer Level (RTL)
  Behavioral
Serve as input for synthesis tools

## Slide 26: Hardware Implementations
HDLs can be compiled to semi-custom and programmable hardware implementations
Standard Cell
Gate Array
FPGA
PLD
Manual VLSI
Full Custom
Semi-Custom
Programmable
less work, faster time to market
implementation efficiency

## Slide 27: Hardware Building Blocks
Transistors are switches
Use multiple transistors to make a gate
Use multiple gates to make a circuit
A
A
A
A
G
D
S

## Slide 28: Standard Cells
Library of common gates and structures (cells)
Decompose hardware in terms of these cells
Arrange the cells on the chip
Connect them using metal wiring
…

## Slide 29: FPGAs
“Programmable” hardware
Use small memories as truth tables of functions
Decompose circuit into these blocks
Connect using programmable routing
SRAM bits control functionality
P
P1
P2
P3
P4
P5
P6
P7
P8
I1
I3
I2
OUT
FPGA Tiles

## Slide 30: What is a Netlist?
A netlist is a ASCII text representation of the interconnect of a schematic
Many Standards Exist:
  Spice Netlist
  EDIF (Electronic Data Interchange Format)
  Structural Verilog Netlist (this is what we will use)
A1
A2
I1
A
B
C
Z
n1
n2
module comb(Z,A,B,C);
input A,B,C;
output Z;
wire n1, n2;
and02d1 A1(n1,A,B);
inv01d1 I1(n2,C);
and02d1 A2(Z,n1,n2);
endmodule
comb
=

## Slide 31
Review: Combinational Logic
Since HDLs try to abstract hardware design, do we even have to consider the hardware?
  Good hardware design requires ability to analyze a problem to find simplifications
  Multiple variables: throughput, area, latency, power
  Finding an optimal hardware implementation is a computationally complex problem. The synthesis tools need guidance on where to start
Optimization issues
  if(x != 0) vs. if((x <= -1) || (x >= 1))
  What hardware might this generate?

## Slide 32: Verilog Module
In Verilog, a circuit is a module.
module decoder_2_to_4 (A, D) ;
input [1:0] A ;
output [3:0] D ;
assign D = (A == 2'b00) ? 4'b0001 :
(A == 2'b01) ? 4'b0010 :
(A == 2'b10) ? 4'b0100 :
(A == 2'b11) ? 4'b1000 ;
endmodule
Decoder
2-to-4
A[1:0]
D[3:0]
2
4

## Slide 33: Verilog Module
module decoder_2_to_4 (A, D) ;
input [1:0] A ;
output [3:0] D ;
assign D = (A == 2'b00) ? 4'b0001 :
(A == 2'b01) ? 4'b0010 :
(A == 2'b10) ? 4'b0100 :
(A == 2'b11) ? 4'b1000 ;
endmodule
Decoder
2-to-4
A[1:0]
D[3:0]
2
4
ports names of module
module name
port types
port sizes
module contents
keywords underlined

## Slide 34: Declaring A Module
Can’t use keywords as module/port/signal names
  Choose a descriptive module name
Indicate the ports (connectivity)
Declare the signals connected to the ports
  Choose descriptive signal names
Declare any internal signals
Write the internals of the module (functionality)

## Slide 35: Good HDL “Self Comments”
35
module xyz123 (A, B) ;
input [3:0] A ;
output B ;
//module contents
endmodule
module doomsday_machine (crystals, earthquake) ;
input [3:0] crystals ;
output earthquake ;
//module contents
endmodule
BAD
GOOD

## Slide 36: Declaring Ports
A signal is attached to every port
Declare type of port
  input
  output
  inout (bidirectional)
Scalar (single bit) - don’t specify a size
  input cin;
Vector (multiple bits) - specify size using range
  Range is MSB to LSB (left to right)
  Don’t have to include zero if you don’t want to… (D[2:1])
  output [7:0] OUT;
  input [0:4] IN;

## Slide 37: Module Styles
Modules can be specified different ways
  Structural – connect primitives and modules
  Dataflow– use continuous assignments
  Behavioral – use initial and always blocks
A single module can use more than one method!
What are the differences?

## Slide 38: Structural
A schematic in text form (i.e. A netlist)
Build up a circuit from gates/flip-flops
  Gates are primitives (part of the language)
  Flip-flops themselves described behaviorally
Structural design
  Create module interface
  Instantiate the gates in the circuit
  Declare the internal wires needed to connect gates
  Put the names of the wires in the correct port locations of the gates
    For primitives, outputs always come first

## Slide 39: Structural Example
module majority (major, V1, V2, V3) ;
output major ;
input V1, V2, V3 ;
wire N1, N2, N3;
and A0 (N1, V1, V2),
A1 (N2, V2, V3),
A2 (N3, V3, V1);
or Or0 (major, N1, N2, N3);
endmodule
V1
V2
V2
V3
V3
V1
major
N1
N2
N3
A0
A1
A2
Or0
majority

## Slide 40: RTL Example
module majority (major, V1, V2, V3) ;
output major ;
input V1, V2, V3 ;
assign major = V1 & V2
| V2 & V3
| V1 & V3;
endmodule
V1
V2
V3
major
majority

## Slide 41: Behavioral Example
module majority (major, V1, V2, V3) ;
output reg major ;
input V1, V2, V3 ;
always @(V1, V2, V3) begin
if (V1 && V2 || V2 && V3
|| V1 && V3) major = 1;
else major = 0;
end
endmodule
V1
V2
V3
major
majority

## Slide 42: FSM Review
Combinational and sequential logic
Often used to generate control signals
Reacts to inputs (including clock signal)
Can perform multi-cycle operations
Examples of FSMs
  Counter
  Vending machine
  Traffic light controller
  Bus Controller
  Control unit of serial protocol (like RS232, I2C or SPI)

## Slide 43: Mealy/Moore FSMs
Next State
Logic
FF
State Register
Inputs
Outputs
Output
Logic
Mealy
Next State
Current State

## Slide 44: FSMs
Moore
  Output depends only on current state
  Outputs are synchronous (but not necessarily glitch free)
Mealy
  Output depends on current state and inputs
  Outputs can be asynchronous
    Change with changes on the inputs
  Outputs can be synchronous
    Register the outputs
    Outputs delayed by one cycle

## Slide 45: Remember Bubble Diagrams?
They can be useful. I sometimes will draw a bubble diagram first for a complex FSM. Then code it.
Given the datapath
For a single slope
A2D converter.
Draw a bubble diagram
For a FSM that can control it.
It should run the converter for 8 times and accumulate the 8 results in a 13-bit register. The upper 10-bits of which are used as the result.
-
+
10-bit
DAC
DAC
Counter
clk
inc_dac
clr_dac
10
Analog_in
gt
13
13
clk
accum
{000,cnt}
13
result
Sample
Counter
inc_smp
clr_smp
Digital
Compare
To 7
smp_eq_8
10
0
1
clk
13

## Slide 46: Things to do
Familiarize self with the Moodle webpage
Look at the IEEE Verilog standard on webpage

## Slide 47: Review Questions
What are some advantages of using HDLs, instead of schematic capture?
What advantages and disadvantages do standard cell designs have compared to full-custom designs?
What are some ways in which HDLs differ from conventional programming languages? How are they similar?
What are the different styles of Verilog coding?